## Slide 1: Acoustic Underwater Communication
Thomas BOUSTON | Elyne FERREIRA DA COSTA | Yashveen JOOTUN
28 / 03 / 2024
Notes: - Thomas -

## Slide 2
Presentation Overview
Introduction and Context
Project Specifications
Technical Solution
Conclusion
Notes: - Thomas -

## Slide 3: Project client: Mooring Solution Startup
Introduction and Context
Directed by two Centrale Marseille engineers
Markets connected devices for boating industry
Sells connected buoy against anchor slippage
Notes: - Elyne -

## Slide 4: Project Context
Introduction and Context
Anchor slippage: source of accidents
Connected buoy: notifies owner
Suitable for leisure boats
Notes: - Elyne -

## Slide 5: Project Objective
Introduction and Context
New technology: anchor-based solution
Key challenge: underwater communication
Present submarine communication proof of concept
Notes: - Elyne -

## Slide 6: POC: two devices communicating underwater
Project Specifications
Constraints
  Minimal distance: 3 meters
  Data transmission frequency: 1 hertz
  Volume of data to send: 1 byte
  Devices on battery
Notes: - Elyne -
Préciser que le POC n’existe pas, qu’on n’a pas eu le temps de tester tout dans son ensemble

## Slide 7: State of Art: existing technologies
Project Specifications
Parameters | Electromagnetic (RF) | Optical | Acoustic
Attenuation | 3,5 – 5 dB/m | 0,39 dB/m | 0,1 – 4 dB/Km
Emitter size | 0,5 meters | 0,1 meters | 0,1 meters
Distance | 10 meters | 100 meters | Kilometers
Waves comparison
Notes: - Elyne -

## Slide 8: Acoustic Signal Transmission
Technical Solution
Emitter transducer
Receiver transducer
Device 1
Device 2
Notes: - Thomas -
Transducer principle: transform an electrical signal into an acoustic signal and conversly

## Slide 9: Acoustic Signal Transmission: testing environment
Technical Solution
Notes: - Thomas -
The working environment

## Slide 10: Acoustic Signal Transmission: resulting signal
Technical Solution
Notes: - Thomas -
The resulting signal
Strong attenuation

## Slide 11: Signal Encoding: Frequency Modulation
Principle
  Representing 0s and 1s
  Alternating signal frequencies
  Creating patterns
Technical Solution
Notes: - Yash -
-send a message microcontroller to another with transducers, signal encoded.
-specific signal patterns were selected to represent binary 0s and 1s
-alterning frequencies inside the signal

## Slide 12: Signal Encoding: Frequency Modulation
Technical Solution
Notes: - Yash -
-this method is called frequency modulation.
-The straightforward approach involved choosing two distinct frequencies and alternating the signal between them.
-blue signal has a higher frequency then the red signal

## Slide 13: Signal Encoding: Frequency Modulation
Technical Solution
Notes: - Yash -
patterns chosen, distiguish the order of the freq
-to determine the pattern encoding for a 1 bit or a 0 bit.
-One method was to provide different magnitude for both frequencies.
-The left plot shows a blue wave with both high magnitude and high frequency
followed by a red wave with both low magnitude and low frequency.
-The right plot shows a blue wave with a low magnitude but high frequency followed by a red wave with a high magnitude but low frequency.

## Slide 14: Signal Generation
Technical Solution
Frequencies selection
  Transducer maximum magnitude at 2MHz
    Bandwidth : 1.5-2.5MHz
    2.22MHz & 1.78MHz
  PWM
  STM32F401RE
Notes: - Yash -
-transducers emit a maximum magnitude signal at 2MHz.
-However, the bandwidth falls within a range from 1.5MHz to 2.5MHz.
-In other words, sending a signal with a frequency close to 2MHz mitigates the strength of the wave but remains usable.
-The selected frequencies : 1.78MHz and 2.22MHz.
-it seemed relevant to use STM32 boards which are better suited for signal generation and signal processing.
-a technique called Pulse Width Modulation (PWM)

## Slide 15: Signal Generation: Amplification
Technical Solution
Principle
  Provide sufficient power
  Quickly discharge the transducer
Notes: - Thomas -
Auxiliary system
Transducer compared to capacitor: add a resistor sized to quickly….

## Slide 16: Signal Reception: Amplification
Technical Solution
Principle
  Amplify small signals
  Gain controlling resistor
  High Gain-Bandwidth product
  (at 2MHz, G=10)
Notes: - Thomas -
G = 1+50k/Rg : pour G = 6 Rg = 50

## Slide 17: Signal Amplification
Technical Solution
Notes: - Thomas -

## Slide 18: Signal Reception: Demodulation
Technical Solution
Notes: - Elyne -

## Slide 19: Signal Reception: Analog Filtering and Stabilization
Technical Solution
Bandpass Fc = 1,8 MHz
Bandpass Fc = 2,2 MHz
Peak Detector
Peak Detector
Analog Filtering
Stabilization
Received signal
To STM32 board
Notes: - Elyne -

## Slide 20: Signal Reception: Rauch Structure & Peak Detector
Technical Solution
Rauch Structure
Peak Detector
  For 1,8 MHz
    R1 = R2 = 1.25043 x 105 Ω
    C1 = C2 = C3 = 1pF
    R3 = 555 Ω
    C4 = 1nF
Notes: - Elyne -

## Slide 21: Signal Reception: Abandoned Idea
Technical Solution
  Components could not operate at 2 MHz
  Initial circuits with 20 kHz received signal
    Used operational amplifier: LPM6132
    Used instrumentation amplifier: INA111
Notes: - Elyne -

## Slide 22: Signal Reception: Digital Filtering
Technical Solution
Principle
  Filter Design tool
  Bandpass filter generation
Notes: - Yash -
-analog filter might not work for very high frequencies, one solution is to use a digital filter.
-Digital filters = systems that perform mathematical operations on signal.
-allows the signal to be modeled as required / any of the physical component mentioned for an analog filter.
-digital filters SOMETIMES introduce delay & can also alter the waveform of the signal.
-MATLAB and the tool Filter Design.

## Slide 23: Signal Reception: Digital Filtering
Technical Solution
Analysis
  Filter response Bode plot
  Filter coefficients
  C language code generation
Notes: - Yash -
-generates Bode plot
-gives the filter coef that defines the behaviour of the filter
-can generate C language code for specific STM32 boards

## Slide 24: Signal Reception: Decoding Half Patterns
Technical Solution
1,8 MHz Signal
Half Pattern Substractions
2,2 MHz Signal
1
2
3
4
  1 bit or 0 bit
1
3
2
4
Pattern Result
Notes: - Elyne -

## Slide 25: Final technical solution
Technical Solution
Notes: - Yash -

## Slide 26: Encountered Difficulties
Conclusion
High cost
High frequency component behaviours
Lack of acoustic expertise
Notes: - Thomas -

## Slide 27: Potential Improvements
Conclusion
  Understanding analog filter behavior over VHF
  In situ experiments & encapsulation
  Message robustness
  Distance measuring mode
Notes: Yash –
-Understanding analog filter:
-refining its structure ensure optimal functionality
-optimizing the performance of the filter.
-In situ trials and transducers adjustment
-Conduct experiments in saline environnement particularly in ocean
-distance higher than 3m
-trying with box encapsulation : transducers echo
-Message robustness :
-reliability
-integrity of the message
-Project specification was to be able to measure distances with the 2 transducer non

## Slide 28
Conclusion
Notes: - Elyne -

## Slide 29
Conclusion
Notes: - Elyne -

## Slide 30: General insights
Conclusion
  Opportunity to open minds
  A lot of uncertainty
  Lack of time
  Unmet specifications
Notes: - Elyne -

## Slide 31: Thank you

## Slide 32: Signal Generation: Amplification
Appendices
Considering the transducer as a capacitor C =1nF
Decharging time :
avec
Notes: - Thomas –

## Slide 33: Signal Reception: Rauch Structure
Appendices
  Canonical Form when C = C1 = C2

## Slide 34: Signal Reception: Rauch Structure
Appendices
  Considering R = R1 = R2 = R3:
  Considering C = 1pF: R

## Slide 35: Signal Reception: Peak Detector
Appendices
  Charging and decharging time :

## Slide 36: Half pattern decoding pseudocode
Appendices
Get result after filtering & comparison // half pattern comparison
if result < 0 then
Red signal magnitude > Blue signal magnitude
else
Blue signal magnitude > Red signal magnitude
end if
if ARefMin −0.1×ARefMin <= result <= ARefMin +0.1×ARefMin then
1/2pattern magnitude = Min signal magnitude
else if ARefMax − 0.1 ∗ ARefMax <= result <= ARefMax + 0.1 ∗ ARefMax then
1/2pattern magnitude = Max signal magnitude
end if